## Slide 1: 18-447 Computer Architecture Lecture 24: Simulation and Memory Latency Tolerance
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 3/30/2015

## Slide 2: Lab 5 Results
Avg: 84.4
Median: 93.8
Std Dev: 19.2
Chart: Bins (percentage)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
 | 2 | 0 | 0 | 0 | 0 | 1 | 5 | 2 | 0 | 4 | 14

## Slide 3: Reminder on Assignments
Lab 6 due this Friday (April 3)
  C-level simulation of data caches and branch prediction
Homework 6 will be due April 10
And, we will have a Midterm II
The course will continue to move quickly… Keep your pace.
Talk with the TAs and me if you need any help.
  We cannot do or debug the assignments for you but we can give you suggestions
  My goal is to enable you learn the material
    You never know when you will use the principles you learn

## Slide 4: Simulation: The Field of Dreams

## Slide 5: Dreaming and Reality
An architect is in part a dreamer, a creator
Simulation is a key tool of the architect
Simulation enables
  The exploration of many dreams
  A reality check of the dreams
  Deciding which dream is better
Simulation also enables
  The ability to fool yourself with false dreams

## Slide 6: Why High-Level Simulation?
Problem: RTL simulation is intractable for design space exploration  too time consuming to design and evaluate
  Especially over a large number of workloads
  Especially if you want to predict the performance of a good chunk of a workload on a particular design
  Especially if you want to consider many design choices
    Cache size, associativity, block size, algorithms
    Memory control and scheduling algorithms
    In-order vs. out-of-order execution
    Reservation station sizes, ld/st queue size, register file size, …
    …
Goal: Explore design choices quickly to see their impact on the workloads we are designing the platform for

## Slide 7: Different Goals in Simulation
Explore the design space quickly and see what you want to
  potentially implement in a next-generation platform
  propose as the next big idea to advance the state of the art
  the goal is mainly to see relative effects of design decisions
Match the behavior of an existing system so that you can
  debug and verify it at cycle-level accuracy
  propose small tweaks to the design that can make a difference in performance or energy
  the goal is very high accuracy
Other goals in-between:
  Refine the explored design space without going into a full detailed, cycle-accurate design
  Gain confidence in your design decisions made by higher-level design space exploration

## Slide 8: Tradeoffs in Simulation
Three metrics to evaluate a simulator
  Speed
  Flexibility
  Accuracy
Speed: How fast the simulator runs (xIPS, xCPS)
Flexibility: How quickly one can modify the simulator to evaluate different algorithms and design choices?
Accuracy: How accurate the performance (energy) numbers the simulator generates are vs. a real design (Simulation error)
The relative importance of these metrics varies depending on where you are in the design process

## Slide 9: Trading Off Speed, Flexibility, Accuracy
Speed & flexibility affect:
  How quickly you can make design tradeoffs
Accuracy affects:
  How good your design tradeoffs may end up being
  How fast you can build your simulator (simulator design time)
Flexibility also affects:
  How much human effort you need to spend modifying the simulator
You can trade off between the three to achieve design exploration and decision goals

## Slide 10: High-Level Simulation
  Key Idea: Raise the abstraction level of modeling to give up some accuracy to enable speed & flexibility (and quick simulator design)
Advantage
  + Can still make the right tradeoffs, and can do it quickly
  + All you need is modeling the key high-level factors, you can omit corner case conditions
  + All you need is to get the “relative trends” accurately, not exact performance numbers
Disadvantage
  -- Opens up the possibility of potentially wrong decisions
  -- How do you ensure you get the “relative trends” accurately?

## Slide 11: Simulation as Progressive Refinement
High-level models (Abstract, C)
…
Medium-level models (Less abstract)
…
Low-level models (RTL with eveything modeled)
…
Real design
As you refine (go down the above list)
  Abstraction level reduces
  Accuracy (hopefully) increases (not necessarily, if not careful)
  Speed and flexibility reduce
  You can loop back and fix higher-level models

## Slide 12: This Course
A good architect is comfortable at all levels of refinement
  Including the extremes
This course, as a result, gives you a flavor of both:
  High-level, abstract simulation (Labs 6, 7, 8)
  Low-level, RTL simulation (Labs 2, 3, 4, 5)

## Slide 13: Optional Reading on DRAM Simulation
Kim et al., “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE Computer Architecture Letters 2015.
https://github.com/CMU-SAFARI/ramulator
http://users.ece.cmu.edu/~omutlu/pub/ramulator_dram_simulator-ieee-cal15.pdf

## Slide 14: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues (e.g., heterogeneous multi-core)

## Slide 15: Upcoming Seminar on DRAM (April 3)
April 3, Friday, 11am-noon, GHC 8201
Prof. Moinuddin Qureshi, Georgia Tech
  Lead author of “MLP-Aware Cache Replacement”
Architecting 3D Memory Systems
  Die stacked 3D DRAM technology can provide low-energy high-bandwidth memory module by vertically integrating several dies within the same chip. (…) In this talk, I will discuss how memory systems can efficiently architect 3D DRAM either as a cache or as main memory. First, I will show that some of the basic design decisions typically made for conventional caches (such as serialization of tag and data access, large associativity, and update of replacement state) are detrimental to the performance of DRAM caches, as they exacerbate hit latency. (…) Finally, I will present a memory organization that allows 3D DRAM to be a part of the OS-visible memory address space, and yet relieves the OS from data migration duties. (…)”

## Slide 16: Required Reading
Onur Mutlu, Justin Meza, and Lavanya Subramanian, "The Main Memory System: Challenges and Opportunities" Invited Article in Communications of the Korean Institute of Information Scientists and Engineers (KIISE), 2015.
http://users.ece.cmu.edu/~omutlu/pub/main-memory-system_kiise15.pdf

## Slide 17: Required Readings on DRAM
DRAM Organization and Operation Basics
  Sections 1 and 2 of: Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
  http://users.ece.cmu.edu/~omutlu/pub/tldram_hpca13.pdf
  Sections 1 and 2 of Kim et al., “A Case for Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
  http://users.ece.cmu.edu/~omutlu/pub/salp-dram_isca12.pdf
DRAM Refresh Basics
  Sections 1 and 2 of Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012. http://users.ece.cmu.edu/~omutlu/pub/raidr-dram-refresh_isca12.pdf

## Slide 18: Readings on Bloom Filters
  Section 3.1 of
    Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
Section 3.3 of
  Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 19: Difficulty of DRAM Control

## Slide 20: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to manage power consumption
Need to optimize performance & QoS (in the presence of constraints)
  Reordering is not simple
  Fairness and QoS needs complicates the scheduling problem

## Slide 21: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 22: More on DRAM Operation
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 23: DRAM Controller Design Is Becoming More Difficult
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 24: Reality and Dream
Reality: It difficult to optimize all these different constraints while maximizing performance, QoS, energy-efficiency, …
Dream: Wouldn’t it be nice if the DRAM controller automatically found a good scheduling policy on its own?

## Slide 25: Self-Optimizing DRAM Controllers
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.

## Slide 26: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.
Goal: Learn to choose actions to maximize r0 + r1 + 2r2 + … ( 0   < 1)

## Slide 27: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 28: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 29: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 30: Performance Results

## Slide 31: Self Optimizing DRAM Controllers
Advantages
  + Adapts the scheduling policy dynamically to changing workload behavior and to maximize a long-term target
  + Reduces the designer’s burden in finding a good scheduling policy. Designer specifies:
  1) What system variables might be useful
  2) What target to optimize, but not how to optimize it
Disadvantages and Limitations
  -- Black box: designer much less likely to implement what she cannot easily reason about
  -- How to specify different reward functions that can achieve different objectives? (e.g., fairness, QoS)
  -- Hardware complexity?

## Slide 32: Memory Latency Tolerance

## Slide 33: Readings on Memory Latency Tolerance
Required
  Mutlu et al., “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors,” HPCA 2003.
  Srinath et al., “Feedback directed prefetching”, HPCA 2007.
Optional
  Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.
  Armstrong et al., “Wrong Path Events,” MICRO 2004.

## Slide 34: Remember: Latency Tolerance
An out-of-order execution processor tolerates latency of multi-cycle operations by executing independent instructions concurrently
  It does so by buffering instructions in reservation stations and reorder buffer
  Instruction window: Hardware resources needed to buffer all decoded but not yet retired/committed instructions
What if an instruction takes 500 cycles?
  How large of an instruction window do we need to continue decoding?
  How many cycles of latency can OoO tolerate?

## Slide 35: Stalls due to Long-Latency Instructions
When a long-latency instruction is not complete, it blocks instruction retirement.
  Because we need to maintain precise exceptions
Incoming instructions fill the instruction window (reorder buffer, reservation stations).
Once the window is full, processor cannot place new instructions into the window.
  This is called a full-window stall.
A full-window stall prevents the processor from making progress in the execution of the program.

## Slide 36: Full-window Stall Example
ADD R2  R2, 64
STOR mem[R2]  R4
ADD R4  R4, R5
MUL R4  R4, R3
LOAD R3  mem[R2]
ADD R2  R2, 8
BEQ R1, R0, target
LOAD R1  mem[R5]
Oldest
L2 Miss! Takes 100s of cycles.
8-entry instruction window:
Independent of the L2 miss,
executed out of program order,
but cannot be retired.
Younger instructions cannot be executed
because there is no space in the instruction window.
The processor stalls until the L2 Miss is serviced.
Long-latency cache misses are responsible for
most full-window stalls.
LOAD R3  mem[R2]

## Slide 37: Cache Misses Responsible for Many Stalls
512KB L2 cache, 500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 38: The Memory Latency Problem
Problem: Memory latency is long
And, it is not easy to reduce it…
  We will look at methods for reducing DRAM latency in a later lecture
    Lee et al. “Tiered-Latency DRAM,” HPCA 2013.
    Lee et al., “Adaptive-Latency DRAM,” HPCA 2014.
And, even if we reduce memory latency, it is still long
  Remember the fundamental capacity-latency tradeoff
  Contention for memory increases latencies

## Slide 39: How Do We Tolerate Stalls Due to Memory?
Two major approaches
  Reduce/eliminate stalls
  Tolerate the effect of a stall when it happens
Four fundamental techniques to achieve these
  Caching
  Prefetching
  Multithreading
  Out-of-order execution
Many techniques have been developed to make these four fundamental techniques more effective in tolerating memory latency

## Slide 40: Memory Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates irregular cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
  Runahead execution alleviates this problem (as we will see today)

## Slide 41: Runahead Execution

## Slide 42: Small Windows: Full-window Stalls
ADD R2  R2, 64
STOR mem[R2]  R4
ADD R4  R4, R5
MUL R4  R4, R3
LOAD R3  mem[R2]
ADD R2  R2, 8
BEQ R1, R0, target
LOAD R1  mem[R5]
Oldest
L2 Miss! Takes 100s of cycles.
8-entry instruction window:
Independent of the L2 miss,
executed out of program order,
but cannot be retired.
Younger instructions cannot be executed
because there is no space in the instruction window.
The processor stalls until the L2 Miss is serviced.
Long-latency cache misses are responsible for most full-window stalls.
LOAD R3  mem[R2]

## Slide 43: Impact of Long-Latency Cache Misses
512KB L2 cache, 500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 44: Impact of Long-Latency Cache Misses
500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 45: The Problem
Out-of-order execution requires large instruction windows to tolerate today’s main memory latencies.
As main memory latency increases, instruction window size should also increase to fully tolerate the memory latency.
Building a large instruction window is a challenging task if we would like to achieve
  Low power/energy consumption (tag matching logic, ld/st buffers)
  Short cycle time (access, wakeup/select latencies)
  Low design and verification complexity

## Slide 46: Efficient Scaling of Instruction Window Size
One of the major research issues in out of order execution
How to achieve the benefits of a large window with a small one (or in a simpler way)?
How do we efficiently tolerate memory latency with the machinery of out-of-order execution (and a small instruction window)?

## Slide 47: Memory Level Parallelism (MLP)
Idea: Find and service multiple cache misses in parallel so that the processor stalls only once for all misses
  Enables latency tolerance: overlaps latency of different misses
How to generate multiple misses?
  Out-of-order execution, multithreading, prefetching, runahead
time
A
B
C
isolated miss
parallel miss

## Slide 48: Runahead Execution (I)
A technique to obtain the memory-level parallelism benefits of a large instruction window
When the oldest instruction is a long-latency cache miss:
  Checkpoint architectural state and enter runahead mode
In runahead mode:
  Speculatively pre-execute instructions
  The purpose of pre-execution is to generate prefetches
  L2-miss dependent instructions are marked INV and dropped
Runahead mode ends when the original miss returns
  Checkpoint is restored and normal execution resumes
Mutlu et al., “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors,” HPCA 2003.

## Slide 49: Runahead Example
Compute
Compute
Compute
Load 1 Miss
Miss 1
Stall
Compute
Load 2 Miss
Miss 2
Stall
Load 1 Hit
Load 2 Hit
Compute
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Hit
Miss 1
Miss 2
Compute
Load 1 Hit
Saved Cycles
Perfect Caches:
Small Window:
Runahead:

## Slide 50: Benefits of Runahead Execution
Instead of stalling during an L2 cache miss:
Pre-executed loads and stores independent of L2-miss instructions generate very accurate data prefetches:
  For both regular and irregular access patterns
Instructions on the predicted program path are prefetched into the instruction/trace cache and L2.
Hardware prefetcher and branch predictor tables are trained using future access information.

## Slide 51: Runahead Execution Mechanism
Entry into runahead mode
  Checkpoint architectural register state
Instruction processing in runahead mode
Exit from runahead mode
  Restore architectural register state from checkpoint

## Slide 52: Instruction Processing in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
Runahead mode processing is the same as normal instruction processing, EXCEPT:
It is purely speculative: Architectural (software-visible) register/memory state is NOT updated in runahead mode.
L2-miss dependent instructions are identified and treated specially.
  They are quickly removed from the instruction window.
  Their results are not trusted.

## Slide 53: L2-Miss Dependent Instructions
Compute
Load 1 Miss
Runahead
Miss 1
Two types of results produced: INV and VALID
INV = Dependent on an L2 miss
INV results are marked using INV bits in the register file and store buffer.
INV values are not used for prefetching/branch resolution.

## Slide 54: Removal of Instructions from Window
Compute
Load 1 Miss
Runahead
Miss 1
Oldest instruction is examined for pseudo-retirement
  An INV instruction is removed from window immediately.
  A VALID instruction is removed when it completes execution.
Pseudo-retired instructions free their allocated resources.
  This allows the processing of later instructions.
Pseudo-retired stores communicate their data to dependent loads.
Notes: Exceptions ignored. I/O operations that modify the state of the I/O devices are not performed. Uncacheable blocks are not fetched.

## Slide 55: Store/Load Handling in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
A pseudo-retired store writes its data and INV status to a dedicated memory, called runahead cache.
Purpose: Data communication through memory in runahead mode.
A dependent load reads its data from the runahead cache.
Does not need to be always correct  Size of runahead cache is very small.

## Slide 56: Branch Handling in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
INV branches cannot be resolved.
  A mispredicted INV branch causes the processor to stay on the wrong program path until the end of runahead execution.
VALID branches are resolved and initiate recovery if mispredicted.

## Slide 57: A Runahead Processor Diagram
Mutlu+, “Runahead Execution,”
HPCA 2003.

## Slide 58: Runahead Execution Pros and Cons
Advantages:
  + Very accurate prefetches for data/instructions (all cache levels)
  + Follows the program path
  + Simple to implement, most of the hardware is already built in
  + Versus other pre-execution based prefetching mechanisms (as we will see):
  + Uses the same thread context as main thread, no waste of context
  + No need to construct a pre-execution thread
Disadvantages/Limitations:
  -- Extra executed instructions
  -- Limited by branch prediction accuracy
  -- Cannot prefetch dependent cache misses
  -- Effectiveness limited by available “memory-level parallelism” (MLP)
  -- Prefetch distance limited by memory latency
Implemented in IBM POWER6, Sun “Rock”

## Slide 59: Performance of Runahead Execution

## Slide 60: Runahead Execution vs. Large Windows

## Slide 61: Runahead vs. A (Real) Large Window
When is one beneficial, when is the other?
Pros and cons of each
Which can tolerate FP operation latencies better?
Which leads to less wasted execution?

## Slide 62: Runahead on In-order vs. Out-of-order

## Slide 63: Effect of Runahead in Sun ROCK
Shailender Chaudhry talk, Aug 2008.